## Slide 1
電信所 林柏呈
NB-IOT自動化定位監測系統應用於貨件追縱之構想

## Slide 2
Outline
Motivation
Concept of Design
Business Model
System Model
      Lora
      MQTT
      Implementation
      Http User Interface
      Future Work

## Slide 3
Motivation
Ref: https://www.jantoo.com/cartoons/keywords/losing-packages

## Slide 4
Concept of Design
將GPS放入貨件
GPS定位貨件位置
位置資料利用Lora傳至鄰近Gateway
資料藉由MQTT傳至網頁伺服器
將資料存置資料庫與網頁前端
隨時瀏覽網頁追蹤貨件位置
貨件送達
GPS寄還寄件者

## Slide 5
Business Model
資訊業者與宅配合作
以每月一期的租約方式出租GPS定位追蹤器。依每期使用次數的不同調整租約費用，業者可依市場需求選擇方案。
使用租約模式之益處：
非隨時需要寄送貴重物品
降低成本
租約可提供宅配固定人工成本

## Slide 6
System Model
Linkit 7688 duo
Lora Gateway
Web Server
LORA
Database
Google Map application
Http Interface
Ublox NEO-6M V2 GPS
(1)
(2)
(3)
(4)
Dragino Lora Sheild
Lora Mote
Arduino Uno
Dragino Lora Sheild
MQTT
(5)

## Slide 7
Lora
low data rate
(range from 0.3 kbps to 50 kbps)
低功耗
長距離 line-of-sight 可以傳到20km遠
長電池壽命
(Bi-directional communication with
Class-A)
Ref: https://read01.com/5xzLQE.html

## Slide 8
MQTT
Allow devices to publish-and-subscribe to
messages being broadcast over an
TCP/IP network.
Messages are simply composed of
a topic and a payload
MQTT can handle everything from Ethernet
to packet sized data to megabytes
Has options for managing unreliable connections
Ref: http://blog.maxkit.com.tw/2014/01/mqtt.html

## Slide 9
Implementation
Lora Mote
Lora Gateway
GPS System

## Slide 10
HTTP User Interface

## Slide 11
Future Work
Linkit 7688 duo
Lora Gateway
Web Server
LORA
Database
Google Map application
Http Interface
Ublox NEO-6M V2 GPS
(1)
(2)
(3)
(4)
Dragino Lora Shield
Lora Mote
Arduino Uno
Dragino Lora Sheild
MQTT
(5)
SIMCOM SIM900 GPRS/GSM Module
(6)
(7)
(8)
(9)
Police Station

## Slide 12: Thanks!